## Slide 1
Tube or not Tube: Manipulation and Sampling Operations on Mars 2020

## Slide 2: Introduction
First part of a two-part series discussing Mars 2020 Robotic Operations based on this paper, which was selected as the Best Paper overall from the 2025 IEEE Aerospace conference:
  V. Verma, M. Maimone, K. Kaplan, E. Thiel, N. Rothenberger, J. Carsten, A. Rankin, E. Schaler, E. Graser, N. Balabanska, S. Kuhn, and H. Dor, "Robotic Operations During Perseverance’s First Extended Mission," 2025 IEEE Aerospace Conference, Big Sky, MT, USA, Winner of M. Charles Fogg Best Conference Paper Award, 02 March 2025.
Today’s talk will focus on robotic arm and sampling challenges and operational improvements
  Robotic Operations Overview (Mark Maimone)
  Abraded Science Optimizations (Joseph Carsten)
  Sampling and Caching Updates (Kyle Kaplan)
  Robotic Arm Force-Torque Sensor Recalibration (Ethan Schaler)

## Slide 3
Mars 2020 Robotic Operations
Mark Maimone

## Slide 4: What does RO do?
The Mars 2020 Robotic Operations (RO) team is responsible for the development, planning and Mars execution of robotics aspects of the mission.
This includes the Perseverance rover’s:
mobility,
manipulation,
Mechanisms,
sampling operations,
Ingenuity helicopter’s flights.
A lesson learned from MER and MSL missions is that these Robotic Operations require a unique approach compared to non-surface deep space missions. Every drive results in a new effective landing site, and issues and ISAs can arise every day, hence the response time needs to be faster. So M2020 created RO as a top-level project organization to support rapid deployment of operations tools and strategies to improve overall mission safety.

## Slide 5: Robotic Operations Org Chart

## Slide 6: RO Impact on Operations
Commands from the Robotic Operations (RO) team execute nearly every day

## Slide 7
Abrasion Sol Path Optimization
Joseph Carsten

## Slide 8: Turret Overview
Facility Contact Sensor (FCS)
Gas Dust Removal Tool (gDRT)
Drill
Wide Angle Topographic Sensor for Operations and eNgineering (WATSON)
Planetary Instrument for X-ray Lithochemistry (PIXL)
Scanning Habitable Environments with Raman & Luminescence for Organics and Chemicals (SHERLOC)
Proximity Science instruments are PIXL, SHERLOC, and WATSON

## Slide 9: Proximity Science
Vast majority of proximity science observations have been performed on abraded surfaces
Abraded surfaces are strongly preferred by the science team
  Removes the outer weathering rind
  Creates a smoother surface for observation
NASA/CalTech-JPL/MSSS

## Slide 10: Placement Challenges
PIXL and SHERLOC must be placed at very small standoffs while maintaining adequate margin to inadvertent terrain contact
  PIXL standoff is 25.5 mm
  SHERLOC context imager is in focus at a 41.3 mm standoff
Abrading makes achieving terrain clearance more difficult
  Need to place the instruments relative to the bottom of a hole (abrasion depths are generally around 7 – 10 mm)
  Abrading creates cuttings piles around the outside of the abraded patch further reducing clearances
Very roughly to scale

## Slide 11: Abrasion Target Analysis
Involves placement of every single tool on the turret
Need to perform clearance analysis for all tool placements (including four different gDRT placements)
Need to evaluate the suitability of the drill placement (surface roughness, debris under the stabilizers, anticipated stabilizer articulation)
Need to verify arm preload is safe to apply
Need to perform a predictive analysis to evaluate the likelihood of being able to perform proximity observations post abrasion

## Slide 12: Abrasion Target Analysis (cont)
Complex abrasion target evaluation could not reliably be performed during the couple hours available on the tactical timeline
Moved to a strategic evaluation requiring augmented staffing
Tactical team captures WATSON target refinement images of candidate targets
  Higher resolution imaging makes it easier to identify small pebbles and other debris
  Reduces uncertainty in the placement of the abraded patch
  Reduced uncertainty makes target evaluation more likely to pass
NASA/CalTech-JPL/MSSS

## Slide 13: Original Abrasion Sol Path
Drive to Approach Target
Navcam and Hazcam Stereo Images
Capture WATSON Target Refinement Images
Abrade, Dust Clearing, Workspace Imaging
PIXL, SHERLOC, WATSON Observations
Sols on Mars
Abrasion Target Evaluation,
Sequence WATSON Imaging
Finalize Abrasion Target, Sequence Abrasion Activities
Evaluate Science Targets, Sequence Proximity Science
Planning Cycles on Earth
WATSON Images
Navcam and Hazcam Stereo Images, WATSON Images

## Slide 14: Target Wizard
Undertook an effort to automate much of the target evaluation process
Evaluations that used to take tens of minutes for a given target can now be done in a few seconds

## Slide 15: Predictive Analysis Risk Posture
Foregoing WATSON refinement images increases placement uncertainty, making it harder to locate a target with high confidence of being able to place proximity science instruments
Instead of using 3 sigma uncertainty (99.7% confidence) for the predictive analysis, use 1.5 sigma (87% confidence)
Makes finding an abradable target without WATSON refinement images only slightly harder than it is with those images
Still use 3 sigma uncertainty for all hardware safety checks
 | Predictive Analysis Lateral Uncertainty
With WATSON refinement, 3 sigma | 11.0 mm
No WATSON refinement, 1.5 sigma | 16.8 mm
No WATSON refinement, 3 sigma | 29.4 mm

## Slide 16: New Abrasion Sol Path
Drive to Approach Target
Navcam and Hazcam Stereo Images
Capture WATSON Target Refinement Images
Abrade, Dust Clearing, Workspace Imaging
PIXL, SHERLOC, WATSON Observations
Sols on Mars
Abrasion Target Evaluation,
Sequence WATSON Imaging
Finalize Abrasion Target, Sequence Abrasion Activities
Evaluate Science Targets, Sequence Proximity Science
Planning Cycles on Earth
Navcam and Hazcam Stereo Images, WATSON Images

## Slide 17: Results
24 abrasions performed between rollout on sol 1079 and sol 1565
Never needed to spend an additional sol to capture WATSON refinement images
Saved 21 planning cycles and completed one abrasion we would not have done without the optimization

## Slide 18
Sampling and Caching Updates
Kyle Kaplan

## Slide 19: Sampling and Caching Subsystem (SCS)
Sampling Stats | 
Abrasions Attempted | 50
gDRT Puffs | 259
Tubes Sealed | 31 (2 filled, but unsealed)
- Rock Cores | 25
- Regolith | 2
- Witness | 3
- Atmospheric | 1
Bit Exchanges | 98
Marmen Abrasion, Sol 1513.
All samples sealed or in storage. Credit: J. Maki
Notes: 1-2 min
Overview of hardware and capabilities
Emphasize progress of mission (e.g. 31 of 41 tubes sealed)

## Slide 20: Extended Mission Sampling Operations
Learning how to drill rocks at the edge of our performance limits.
CORING_3 Mushroom, Sol 371.
Pauls sample dump, Sol 325.
Rover selfie, Sol 1500.
Releasing new capabilities to enable increased science return.
Gallants coring attempt, Sols 1551-1552.
Abrading Drakes Point, Sol 1565.
Gallants post-coring, Sol 1555.
Notes: 2 min
Challenges of attempting to keep up with Science’s requests
Using the system in ways that have not necessarily been tested on Earth and seeing varying degrees of success
Want to get the most out of the hardware and maximize Science return
Using the hardware in ways that were considered before ops but not fully exercised (e.g. sample dump)

## Slide 21: Gas Dust Removal Tool (gDRT) Operations
Rotational angle of 120°
Angle relative to normal of 15°
Lateral offset of 5 mm
Vertical offset of 80 mm
Mass of gas of ~0.1g per shot
Adjust plenum pressure and on time based on temperature
Vertical offset of 80 mm
Mass of gas of ~0.1g per shot
Adjust plenum pressure and on time based on temperature
Vent plenum.
Fill plenum.
“Triplets” puff 1.
Refill plenum.
“Triplets” puff 2.
Refill plenum.
“Triplets” puff 3.
Refill plenum.
Normal puff.
Guillames abrasion after gDRT puffs, Sols 159-160.
PRT
Notes: 1 min
Explain how abrading + gDRT enables prox sci
Brief overview of gDRT hardware and how system is used in ops

## Slide 22: gDRT Budget Error
Notes: 2 min
Describe the 3 methods of gas budgeting and what the budgets showed in the first few puffs
Point out why this was concerning – what the life req. is and how much gas we thought we filled to
Explain concept of isochoric lines on P-T plot and how some data points deviated from this even when the system wasn’t in use
Began separating out use data (noisy) from read data (more consistent, but very little of it)
Change in pressure read strategy – intentionally collect data in between uses and at differing temperatures (begin to plot isochor)
Found out that temperature and rate of change in temperature resulted in poor pressure estimates – lead into next slide

## Slide 23: gDRT Budget Error Resolution
Notes: Explain inconsistencies with temperature data due to PRT placement on tank boss and temp lag
Point out filtered out data points based on PRT thresholds
Describe concept of latest density using most recent data points from read periods (“zero out” error)
Emphasize that there is more than sufficient gas to achieve Science mission

## Slide 24
In-Situ Recalibration of a 6-DoF Force / Torque Sensor
Ethan Schaler

## Slide 25: Force / Torque Sensor Overview

## Slide 26: Force / Torque Sensor Overview
Interface to Turret Actuator (proximal)
Interface to Turret Output Plate (distal)
Turret Actuator
Turret Mass Model
Turret Output Plate
Fx
Fy
tx
Fz
ty
tz
Sensor Frame

## Slide 27: FTS Calibration Models
sg1 to sg6 are the strain gauges values in mV/V
t0 is the FTS PRT temperature in deg C
Offset
Coeff.
Linear Coeffs.
Temp
Coeff.
Nonlinear Coeffs.
Linear Coeffs.
Offset Coeff.

## Slide 28: Pre-Landing Calibration Strategy

## Slide 29: Pre-Landing Calibration Performance
System-Level calibration successfully eliminated significant cross-coupling, thermal effects, and other error sources, versus a Sensor-Level calibration.
Sensor-Level Calibration
System-Level Calibration
Colored by FTS temperature from –70 degC (blue) to +22 degC (red)

## Slide 30: After ~1 Mars Year
Visible time-dependent offset drift in residual error (primarily on FZ) – all data taken at similar warm temp, but over time and colored by Sol #
FTS-A Error (colored by Sols 18 – 621)
FTS-B Error (colored by Sols 18 – 621)
Blue is Sol 18 data
Grey is Sol 287 data
Red is Sol 621 data

## Slide 31: After ~1 Mars Year
Visible non-linear, temperature-dependent error (primarily on FZ) – data from identical checkouts run at 3 temperatures over 26 Sols
FTS-A (colored by Temp, Sols 595 – 621)
FTS-B (colored by Temp , Sols 595 – 621)
Blue is -71 degC data
Grey is -40 degC data
Red is -15 degC data

## Slide 32: In-Situ Calibration Strategy
Problem: How do you recalibrate an FTS in-situ? Unlike science instruments, there are no dedicated calibration targets…
Strategy: We again use the turret weight gravity model as a truth load, and we find a calibration that minimizes the residual error to this truth load.
Modify – not replace – the preceding system-level calibration
Dataset is collected by (carefully) waving the turret + wrist about for 1 hour
Constraints: limited load ranges + coupled loads, temperatures by time-of-day

## Slide 33: In-Situ Calibration Results
Colored by FTS temperature from -70 degC (blue) to -15 degC (red)
FZ (before in-situ calibration)
FZ (after in-situ calibration)

## Slide 34: Impact of In-Situ Calibration on Fault Case

## Slide 35: Continuing Operations on Mars
The In-Situ Calibration was uplinked to the rover on Sol 881 and has successfully been running on Mars since then (now Sol 1600+).
Ongoing trending of FTS performance:
Quarterly trending of margin to fault protection limits
FTS checkout exercise every Martian summer / winter

## Slide 36: Sneak Peek
The next Mission Chronicles talk will continue the discussion of Mars 2020 Robotic Operations on September 18, 2025 and will cover:
Mobility
Record-setting drives! 90% of all driving has been autonomous!
Mechanisms
Dealing with faults that occur due to specific terrains
Next steps for Ingenuity
A look into the post-flight use of Ingenuity and supporting hardware
Technology Development
Using commercial Snapdragon CPU for Global Localization on Mars

## Slide 37: Q & A
Questions? Answers!
To be called on for a question, please raise your hand in Teams or go to a microphone in the auditorium

## Slide 38
Backup

## Slide 39: Lessons Learned
Some of the Lessons Learned during this period:
Success in extended mission by designing for the unknown
  Robotics software leaves hooks for future capabilities, parameters to control processing
Integrated System Verification & Validation and ground software dependencies delay new technology deployment
  Flight-based Global Localization was delayed for months by ground tool deployment
Prepare for recalibration
  Fiducials, sensor redundancy
Include all teams in flight software scheduling
  Original plan did not account for substantial robotics test time
Grouping brake channels is not so simple
  Come to the next talk for details!
Future missions can have ripple effects
  MSR changes necessitated additional life tests, disabling VSTB mobility for months

## Slide 40: PIXL Placement Example
11 mm abrasion depth
3.5 mm tailings height
25.5 mm
11 mm